## Slide 1
Master Thesis
Architecture Development to Replace Finite Element Methods with Deep Neural Networks
Examiners:
Prof. Dr. – Ing. Andreas Schwung & Prof. Dr. – Ing. Jens Oberrath
Advisor:
MSc. Johannes Pöppelbaum
Presented by:
Kaushal Narendra Tare
(10062903)

## Slide 2
Introduction
Computer Aided Engineering (CAE)
The use of computer software to simulate performance in order to -
Improve product design
Assist in resolution of engineering problems
1

## Slide 3
FEM is a numerical method used to obtain the approximate solution in CAE
Most systems can be mathematically represented by differential equations
Analytical solution is easy to calculate for simple geometries and difficult for complex geometry
Finite Element Method (FEM)
2
System

## Slide 4
Continuous System
Discrete System
Elements
Nodes
Meshing
Perform elementwise calculations
Assemble and obtain values at nodes for the entire domain
Obtain field solution for the entire domain
The FEA Procedure (Practical visualization)

## Slide 5
Limitations of FEA
Re-running the complete scenario for slightest change in the inputs (time consuming)
Highly complex scenarios are computationally expensive
Machine Learning as a Solution
ML model learns relation between inputs and outputs from historical simulation data
Predicts the new simulation scenario based on learned relations
ML Model
Knowledge Base
Data from past FE simulation runs
Train
New/similar scenario
ML model predicted output

## Slide 6
Deep Learning
3
Graph Neural Networks
Data structure consisting of nodes and edges
Structural analogy with discrete system in FEM
A discrete system can be modelled as graph network
Continuous System
Discrete System
Elements
Nodes
Meshing
Graph Network
Nodes
Edges

## Slide 7
Computation Graph
Working of GNNs
A
B
D
C
F
E
Gather locality information
Aggregate and compute the information through multiple layers
Obtain the final node embeddings
similarity
encode nodes
Embedding space
A
B
D
C
F
E

## Slide 8
A rigid structural element supported at one end and free at other
Case Study Scenario: Cantilever Beam
4
Applications:
Aesthetic roofs
Cranes
Span of bridges
Aircraft wing

## Slide 9
Model the discrete system to GNN
Input node features as sequence of forces
Graph computations through multiple GNN layers
Pass the final node embeddings to MLP
Obtain output deformation and stress
Building the DNN Model
5
Cantilever beam discrete system
Graph Network
DNN pipeline

## Slide 10
Deformation (mm) at time step 1
predicted
actual
Deformation (mm) at time step 2
predicted
actual
Deformation (mm) at time step 3
predicted
actual
Deformation (mm) at time step 4
predicted
actual
Deformation (mm) at time step 5
predicted
actual
3D Deformation Plots
Excellent deformation prediction
Experiment Results

## Slide 11
Deformation Error Visualization
Deformation error varies between -1 to +1.5 mm
Relative error is close to zero for higher deformation values at the free end

## Slide 12
Stress (MPa) at time step 1
Stress (MPa) at time step 2
Stress (MPa) at time step 3
Stress (MPa) at time step 4
Stress (MPa) at time step 5
Stress Distribution Plots
The stress concentration regions are rightly predicted by the model

## Slide 13
Stress Error Visualization
Stress error varies between -40 to +40 MPa
Relative stress error is close to zero for higher stress values

## Slide 14
Time Analysis
FE Simulation time for 300 rows
DNN computation time for 300 rows
112.5 hrs
9 min

## Slide 15
Conclusion
Model with GCN architecture replicates the FEM results obtained from the simulation software, thus capable of replacing FEM based simulation
Required computation time for DNN model is very less as compared to FE simulation software
Conclusion
7

## Slide 16
Thank You!
Any questions?