## Slide 1: Systems Engineering: Assignment Review Comparison of Data-driven Fault Detection and Identification Methods for the Tennessee Eastman Process
Presented by:
Avadhoot Adawale (10062927),
Kaushal Tare (10062903)
5 February 2018

## Slide 2: Fault Detection & Identification
Faults within process lead to deviation from normal behavior of plant and lower the performance of overall system
Fault Detection:
  Discovers abnormalities in process
Data Driven FD:
  Use of Data analysis tools on evaluation of production data for process monitoring

## Slide 3: Fault Detection & Identification
Benefits of Fault Detection and Identification
  Prediction about expected maintenance
  Improves plant efficiency
  Avoids unnecessary shutdowns
  Ensures safety and reliability of process

## Slide 4: Tennessee Eastman Process ( TEP )

## Slide 5: Tennessee Eastman Process ( TEP )
Major Unit Operations
    Reactor
    Product Condenser
    Vapor Liquid Separator
    Recycle Compressor
    Product Stripper

## Slide 6: Tennessee Eastman Process ( TEP )
21 Pre-programmed Faults
52 Variables
  22 Process Measurement Variables, 19 Composition Measurement Variables, 11 Manipulated Variables
Generate simulated data at an interval of 3 minutes
Normal-Train Data: 500 Samples
Normal-Test Data: 960 Samples
Fault-Train Data: 480 Samples
Fault-Test Data: 960 Samples
  The first 160 samples of fault-test data are normal conditions

## Slide 7: SVM
Finding the best decision boundary that will help separate the classes
Optimum decision boundary has maximum distance from closest points in each class i.e highest 2𝛿
The closest points are known as support vectors
hyperplane: <w,x> + b = 0
𝛿
2𝛿

## Slide 8: SVM – Kernel
If data is not linearly separable then linear classifier is not suitable
Project the data to higher dimension where it can be linearly classified
Kernel function allows computation in more efficient way
Linear
Rbf
Polynomial

## Slide 9: Implementation of SVM in Python
Importing the libraries
Importing the dataset
Feature Scaling
Building the model
Improving the model performance (Tuning the Hyperparameters)
Predicting the test set results
C
Kernel
Degree
Gamma

## Slide 10: Performance Metrics
Confusion matrix and Accuracy on test set
K-fold cross validation

## Slide 11: SVM Results for Fault Cases

## Slide 13: Decision Trees
The model uses if-then-else rules to interpret the value of target variable
Most important attribute is placed at root node
Data is split into subsets to get homogeneous sample
Final data attribute which cannot be classified further is known as leaf

## Slide 14: Decision Trees – Splitting, Pruning
Splitting is done based on-
Information Gain: Difference in entropies
Gini Index: Quantifying amount of uncertainty (impurity) in data
Prone to overfitting due to excessive splitting of data
Pruning makes model simpler, generalized and avoids overfitting
Pruning done by reducing depth of tree by replacing bad branches (subtrees) by leaves

## Slide 15: Implementation of Decision Trees in Python
Importing the libraries
Importing the dataset
Feature Scaling
Building the model
Improving the model performance (Tuning the Hyperparameters)
Criterion
Max_depth
Min_samples_leaf
Predicting the test results

## Slide 16: Performance Metrics
Confusion matrix and Accuracy on test set
K-fold cross validation

## Slide 17: Decision Trees Results for Fault Cases

## Slide 19: Neural Networks
Human Brain

## Slide 20: Neural Networks
Artificial Neural Network

## Slide 21: Neural Networks
Basic Working

## Slide 22: Neural Networks
Learning: W and θ are adjusted, to minimize the error

## Slide 23: Neural Networks
Backpropagation

## Slide 24: Implementation of NN in Python
1. Importing the libraries
2. Importing the dataset
3. Feature Scaling

## Slide 25: Implementation of NN in Python
4. Fitting DNN to training set

## Slide 26: Implementation of NN in Python
- Classifier: Sequential
Layer: Dense
  1. Output Dimension = 26
  2. Init = Uniform
  3. Activation = ReLu (for Hidden Layers) & Sigmoid (for Output Layer)
4. Fitting DNN to training set

## Slide 27: Implementation of NN in Python
Compiling the ANN
  1. Optimizer = adam
  2. Loss = Binary Crossentropy
  3. Activation = ReLu (for Hidden Layers) & Sigmoid (for Output Layer)
4. Fitting DNN to training set

## Slide 28: Implementation of NN in Python
4. Fitting DNN to training set
Fitting the ANN to the training set
  1. Batch Size = 10, 40, 100
  2. Epoch = 100

## Slide 29: Implementation of NN in Python
5. Predicting test results

## Slide 30: Implementation of metrics to measure performance of DNN
1. Confusion Matrix
For Fault 1

## Slide 31: Test and Validation Results for Fault Cases
Fault 1,4,5,7,11 (Combined) (for Batch Size 10)

## Slide 32: Test and Validation Results for Fault Cases
Fault 1, 2, 4 (Combined) (for Batch Size 10)

## Slide 33: Test and Validation Results for Fault Cases

## Slide 34: Detailed Comparison
SVM | Decision Trees | Deep Neural Network
Not biased by outliers Kernel SVM has high performance on non-linear problem | No need of feature scaling Works on both - linear and non-linear cases | Different algorithms can be used for training
Not the best choice for large number of features | Poor results on too small dataset Prone to Overfitting | Require large dataset and computational power
In General:

## Slide 35: Conclusion
The performance of all three classifiers is above the baseline accuracy in all fault cases except 3, 9, 11 and 15.
On comparing the performance, it can be concluded that Deep Neural Network model gives the best accuracy in most cases followed by the SVM and Decision Tree respectively.
The accuracy of classifiers decreases with increase in number of class labels.